## Slide 1: OpenFlow and Software Defined Networks
Notes: <number>

## Slide 2: Outline
The history of OpenFlow
What is OpenFlow?
Slicing OpenFlow networks
Software Defined Networks
Industry interest

## Slide 3: Original Question
How can researchers on college campuses test out new ideas in a real network, at scale?

## Slide 4: Problem
  Many good research ideas on college campuses…
  No way to test new ideas at scale, on real networks, with real user traffic
  Consequence: Almost no technology transfer

## Slide 5: Research problems
Well known problems
  Security, mobility, availability
Incremental ideas
  Fixing BGP, multicast, access control, Mobile IP, data center networks.
More radical changes
  Energy management, VM mobility, …

## Slide 6: How to build a test network with sufficient scale and realism?

## Slide 7: Software Router
PC
+
Multi-Port NIC
Total capacity: Only ~5Gb/s
Notes: <number>

## Slide 8: Custom Hardware
Difficult to develop, always behind industry
Difficult to program, constrained environment
Too expensive
Notes: <number>

## Slide 9: Modify Existing Equipment
Million of lines of source code
6,000 RFCs
Billions of gates
Bloated
Power Hungry
Vertically integrated, complex, closed, proprietary
Not suitable for experimental ideas
Specialized Packet Forwarding Hardware
Operating
System
Feature
Feature
Routing, management, mobility management, access control, VPNs, …
Notes: <number>

## Slide 10
The only test network large enough to evaluate future Internet technologies at scale, is the Internet itself.
Notes: <number>

## Slide 11
OpenFlow Protocol
Data Path (Hardware)
Control Path
OpenFlow
Controller (Server Software)
App
App
App
Notes: <number>

## Slide 12: Slicing traffic
All network traffic
Research
traffic
Experiment #1
Experiment #2
…
Experiment N

## Slide 13: OpenFlow Basics
Notes: <number>
<number>

## Slide 14: Step 1: Separate Control from Datapath
Research Experiments
Notes: <number>

## Slide 15: Step 2: Cache flow decisions in datapath
“If header = x, send to port 4”
“If header = ?, send to me”
“If header = y, overwrite header with z, send to ports 5,6”
Flow
Table
Notes: <number>

## Slide 16: Plumbing Primitives <Match, Action>
Match arbitrary bits in headers:
  Match on any header, or new header
  Allows any flow granularity
Action
  Forward to port(s), drop, send to controller
  Overwrite header with mask, push or pop
  Forward at specific bit-rate
<number>
Header
Data
Match: 1000x01xx0101001x

## Slide 17: General Forwarding Abstraction
Small set of primitives
“Forwarding instruction set”
Protocol independent
Backward compatible
Switches, routers, WiFi APs, basestations, TDM/WDM

## Slide 18: Slicing an OpenFlow Network

## Slide 19: Ways to use slicing
Slice by feature
Slice by user
Home-grown protocols
Download new feature
Versioning

## Slide 21: Research Examples (See openflow.org/Research for demo videos)

## Slide 22: Broader interest in an evolvable Internet

## Slide 23: Restructured Network
Specialized Packet Forwarding Hardware
Feature
Feature
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Specialized Packet Forwarding Hardware
Operating
System
Operating
System
Operating
System
Operating
System
Operating
System
Network OS
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature
Feature

## Slide 24: Software-Defined Network
Feature
Feature
Network OS
1. Open interface to packet forwarding
3. Well-defined open API
2. At least one Network OS probably many. Open- and closed-source
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding
Packet
Forwarding

## Slide 25: Network OS
Research
  NOX (C++/Python) http://noxrepo.org
  Maestro (Rice University)
  Helios (NEC)
  Beacon (Java) coming soon.
  Others in development
Commercial
  ONIX [OSDI 2010, Google, Nicira, NEC]
  Expect others

## Slide 26: Cellular industry
Recently made transition to IP
Billions of mobile users
Need to securely extract payments and hold users accountable
IP sucks at both, yet hard to change
OpenFlow provides a way for the cellular industry to solve real problem plaguing their networks.

## Slide 27: Telco Operators
Global IP traffic growing 40-50% per year
End-customer monthly bill remains unchanged
Therefore, CAPEX and OPEX need to reduce 40-50% per Gb/s per year
But in practice, reduces by ~20% per year
And based on the same equipment as competitors
OpenFlow allows telcos to reduce CAPEX, OPEX and to add new differentiating features to their networks.

## Slide 28: Example: New Data Center
Cost
200,000 servers
Fanout of 20  10,000 switches
$5k vendor switch = $50M
$1k commodity switch = $10M
Savings in 10 data centers = $400M
Control
More flexible control
Tailor network for services
Quickly improve and innovate
Data center companies have been the first to deploy OpenFlow in their networks.

## Slide 29: Next Steps

## Slide 30: OpenFlow Standardization
Version 1.0: Most widely used version
Version 1.1: Released in February 2011.
OpenFlow transferred to ONF in March 2011.

## Slide 31: Thank you!